| Nore Microwave Ltd CV1881 argon-filled noise source The device measures 225x14mm overall. Filament voltage 6.3V Filament current 400mA Striking voltage on DC 1000V Normal operating voltage (Ia=180mA) 60V Max operating current 250mA Nominal continuous operating current 180mA Nominal noise power (Ia=180mA) 15.5db Nominal noise power output change with current -0.005 db/mA Nominal useful working frequency 3GHz-12GHz Nominal gas pressure 30mm |  |
| --- | --- |
| Pictured here is the mount associated with the CV1881 noise tube. Data attached to the mount states ENR at 180 mA, 9 GHz = 15.396 dB, 10 GHz = 15.389 dB. Mount pictures provided by and copyright Wim Ton. |